## Slide 1: Atmospheric stability effects in FLORIS: how to add shear and veer? Pieter 11/25/2015

## Slide 2
 Measured somewhere here :
In a stable atmosphere (hot above cold air), less mixing between lower and upper atmosphere, thus Earth-rotation induced wind direction not propagated to upper atmosphere  wind veer (wind direction shear)
COLD
From: Effects of Complex wind regimes on Turbine Performance, Garrad Hassan America, Inc. AWEA WINDPOWER 2009
Earth rotating
that way
very little mixing here..
my understanding of this…
Stable Atmosphere  Wind Veer
WARM

## Slide 3
From Matt’s poster:
Large-Eddy Simulations of Wind Turbine Wakes Subject to Different Atmospheric Stabilities
Wind Veer  Wake In-Plane Skew
Now: how to characterize wind veer  wake in-plane skew effect in FLORIS?
Also, shear profile is important to take into account (fully 3D FLORIS)

## Slide 4: Skewing a circle..
ellipse/circle with initial height hs and width ws and skew c, can be represented as rotated ellipse with angle phi, width w, height h
phi = atan((c^2*hs^2 - hs^2 + ws^2 + sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))/(2*c*hs^2));
w = sqrt(hs^2*ws^2*(4*c^2*hs^4 + (c^2*hs^2 - hs^2 + ws^2 + sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))^2)/(4*c^2*hs^6 + 2*c^2*hs^4*(4*c^2*hs^4 + (c^2*hs^2 - hs^2 + ws^2 + sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))^2)*(c^2*hs^2 - hs^2 + ws^2 + sqrt(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + hs^4 - 2*hs^2*ws^2 + ws^4))/(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + c^2*hs^2*sqrt(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + hs^4 - 2*hs^2*ws^2 + ws^4) + hs^4 - 2*hs^2*ws^2 - hs^2*sqrt(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + hs^4 - 2*hs^2*ws^2 + ws^4) + ws^4 + ws^2*sqrt(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + hs^4 - 2*hs^2*ws^2 + ws^4)) + c^2*hs^2*(c^2*hs^2 - hs^2 + ws^2 + sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))^2 + ws^2*(c^2*hs^2 - hs^2 + ws^2 + sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))^2))/2;
h = sqrt(hs^2*ws^2*(4*c^2*hs^4 + (c^2*hs^2 - hs^2 + ws^2 - sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))^2)/(4*c^2*hs^6 + 2*c^2*hs^4*(4*c^2*hs^4 + (c^2*hs^2 - hs^2 + ws^2 - sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))^2)*(c^2*hs^2 - hs^2 + ws^2 - sqrt(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + hs^4 - 2*hs^2*ws^2 + ws^4))/(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 - c^2*hs^2*sqrt(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + hs^4 - 2*hs^2*ws^2 + ws^4) + hs^4 - 2*hs^2*ws^2 + hs^2*sqrt(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + hs^4 - 2*hs^2*ws^2 + ws^4) + ws^4 - ws^2*sqrt(c^4*hs^4 + 2*c^2*hs^4 + 2*c^2*hs^2*ws^2 + hs^4 - 2*hs^2*ws^2 + ws^4)) + c^2*hs^2*(c^2*hs^2 - hs^2 + ws^2 - sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))^2 + ws^2*(c^2*hs^2 - hs^2 + ws^2 - sqrt((c^2*hs^2 + hs^2 - 2*hs*ws + ws^2)*(c^2*hs^2 + hs^2 + 2*hs*ws + ws^2)))^2))/2;
Thanks SymPy!

## Slide 5: Including wind shear in FLORIS
Simply apply shear profile as taken from SOWFA (wind speed scaling with height, relative to hub-height speed)
Might use parametric formulations later [link]

## Slide 6: Estimating the skew from wake contours
Take contour plot of wake velocity at cut-throughs with shear removed
Estimate phi from left-upper point of wake contour to calculate skew

## Slide 7: Estimated skew vs. distance to rotor

## Slide 8: Finally, tune recovery of each wake zone to find velocity profiles